HW2
GND
GND
GND
ENABLE
GND
GPI046
INPUT ONLY
-
3V3
GND
BOOT
WS2812
LED-SIG
PHOTORESISTOR
I2C-SDA
I2C-SCL
<available>
SQW
BTN
TOUCHSCREEN_YP_ADC
TOUCHSCREEN_XM_ADC
GPIO0
GND
RTC_GPIO0
-
-
GPIO1
GPIO45
TOUCH1
ADC1_CH0
RTC_GPIO1
UART-RX
UART-TX
BUZZER-SIG
DC-DISPLAY
MISO
SCK
MOSI
U0_RXD
GPIO2
GPIO44
TOUCH2
ADC1_CH1
RTC_GPIO2
!
U0_TXD
GPIO3
GPIO43
TOUCH3
ADC1_CH2
RTC_GPIO3
!
MTMS
GPIO4
GPIO42
TOUCH4
ADC1_CH3
RTC_GPIO4
!
GPIO5
GPIO41
TOUCH5
ADC1_CH4
RTC_GPIO5
MTDI
!
GPIO6
GPIO40
TOUCH6
ADC1_CH5
RTC_GPIO6
!
MTDO
GPIO7
GPIO39
TOUCH7
ADC1_CH6
RTC_GPIO7
!
MTCK
GPIO8
GPIO38
TOUCH8
ADC1_CH7
RTC_GPIO8
GPIO9
GPIO37
FSPI_MISO
TOUCH9
ADC1_CH8
RTC_GPIO9
FSPI_CLK
GPIO10
GPIO36
TOUCH10
ADC1_CH9
RTC_GPIO10
GPIO11
GPIO11
GPIO11
GPIO35
FSPI_MOSI
TOUCH11
TOUCH11
ADC2_CH0
ADC2_CH0
RTC_GPIO11
RTC_GPIO11
B
B
GND
GND
-
-
-
Do Not Use
Have default behavior
Okay to use
-
!
- ADC1 is unaffected with active WiFi while ADC2 gets affected
- FSPI default pins have higher 80MHz SPI frequency
- GPIO19/20 are USB D+/D-
- GPIO43/44 are UART Tx/Rx
- GPIO26 is unavailable on modules with PSRAM
- GPIO46 is input only
Strapping Pins
GPIO0 – Pull-Up
GPIO45 – Pull-Down
GPIO46 – Pull-Down
Hold GPIO0 LOW to enter Download Mode
GPIO12
RTC_GPIO12
ADC2_CH1
TOUCH12
GPIO13
RTC_GPIO13
ADC2_CH2
TOUCH13
GPIO14
RTC_GPIO14
ADC2_CH3
TOUCH14
GPIO15
RTC_GPIO15
ADC2_CH4
GPIO16
RTC_GPIO16
ADC2_CH5
GPIO17
RTC_GPIO17
ADC2_CH6
GPIO18
RTC_GPIO18
ADC2_CH7
GPIO19
RTC_GPIO19
ADC2_CH8
GPIO20
RTC_GPIO20
ADC2_CH9
GPIO21
RTC_GPIO21
GPIO26
NC
GPIO33
GPIO34
GND
USB_D-
USB_D+
DAC_2
U1_RXD
DAC_1
U1_TXD
XTAL_32K_P
XTAL_32K_N
FSPI_CS
UNAVAILABLE ON PSRAM MODULE
Debug
USB-D+
USB-D-
BL
TOUCHSCREEN_YM
TOUCHSCREEN_XP
CS-DISPLAY
RES-DISPLAY

---
TX
RX
----------
DC
RES

---
HW1
INC-BTN
DEC-BTN
WIFI-LED
TOUCHSCREEN_XM_ADC/<available>
TS-CS
TOUCHSCREEN_XP/<available>
TOUCHSCREEN_YM/<available>
TS-IRQ